## Slide 1
6. Trouble Shooting Guide
-53-

## Slide 2
Breakthrough Innovation
HVAC & Energy Solution
6.Trouble Shooting Guide
①
You can find trouble shooting guide in General Service Manual on the web
1. Go to Inventory > Parts Portal
2. Search the model name.
3. Go to ‘Technical Pack’ and select ‘Service Manual’.
4. From there, General Service Manual can be downloaded to your computer.
6.1.1 How to Download a Service Manual
②
③
-54-

## Slide 3
Breakthrough Innovation
HVAC & Energy Solution
6.Trouble Shooting Guide
Operating frequency of compressor depends on the load condition, like the difference between the room
temperature and the set temperature, frequency restrictions.
If the compressor operates at some frequency, the operating frequency of compressor cannot be changed
within 90 seconds(except in emergency conditions).
Compressor turned off when;
- Intake air temperature reaches below 0.5°C(1°F) of the setting temperature for 3 minutes continuously.
- Intake air temperature reaches below 1.5°C(3°F) of the setting temperature
Compressors 3 minutes time delay.
- After compressor off, the compressor can restart minimum 3 minute later.
6.1.2 Introduction to Basic Mode Controls
3
Operating frequency of compressor depends on the load condition, like the difference between the room
temperature and the set temperature, frequency restrictions.
If the compressor operates at some frequency, the operating frequency of compressor cannot be changed
within 30 seconds.
Condition of Compressor turned off when;
- Intake air temperature reaches +3℃ above the setting temperature.
Condition of Compressor turned on when;
- Intake air temperature reaches +2℃above the setting temperature.
While in defrost control, the indoor and outdoor fans are turned off.
■ Heating Mode
■ Cooling Mode
-55-

## Slide 4
Breakthrough Innovation
HVAC & Energy Solution
2.5 Compressor Frequency Restriction
Outdoor Temp (℃) | Cooling (Max Hz) | Outdoor Temp (℃) | Heating (Max Hz)
Outdoor ≤ 0 | 39 | Outdoor ≤ -7 | 107
0< Outdoor ≤10 | 39 | -7< Outdoor ≤-2 | 104
10< Outdoor ≤ 23 | 43 | -2< Outdoor ≤ 4 | 100
23< Outdoor ≤ 30 | 78 | 4< Outdoor ≤ 10 | 97
30< Outdoor ≤40 | 82 | 10< Outdoor ≤21 | 87
46< Outdoor ≤10 | 75 | 21< Outdoor ≤27 | 59
46< Outdoor | 66 | 27< Outdoor | 48
-One of the many frequency restrictions is outdoor temperature limit.Since every model has its own characteristics, Hz varied according to each models.Take Libero R(AS-W126B1U0) for example;
(Max Hz:107, Min Hz:39)
2.6 Comp Operating Hz / Variation of Outdoor Temperature
1. Max Hz reach time(Heating/Standard Condition) : 330secs
2. High Pressure Condition : 39Hz
3. Preheating Mode(39Hz) Reach time(Low Ambient) : / Around 420secs
Outdoor
Outdoor
Outdoor
Outdoor
Outdoor
High
Pressure
2. Basic Operating System
-56-

## Slide 5
Breakthrough Innovation
HVAC & Energy Solution
6.Trouble Shooting Guide
■ Healthy dehumidification operation
When the dehumidification operation is set by the remote controller, the intake air temperature is
detected and the setting temp. is automatically set according to the intake air temperature.
When intake air temp. is 1°C (2°F) above the setting temp., condition of compressor is same as
in cooling mode operation.
When intake air temperature reaches 1°C(2°F) below the setting temp., compressor operates in
step1~step3 and the indoor fan speed again operates at low speed or comes to a stop.
Intake air Temp. | Setting Temp.
26°C(78.8°F) ≤ intake air temp. | 25°C(77°F)
24°C(75.2°F) ≤ intake air temp.< 26°C(78.8°F) | intake air temp. -1°C(-2°F)
22°C(71.6°F) ≤ intake air temp. < 24°C(75.2°F) | intake air temp. -0.5°C(-1°F)
18°C(64.4°F) ≤ intake air temp. < 22°C(71.6°F) | intake air temp.
intake air temp. < 18°C(64.4°F) | 18°C(64.4°F)
■ Cooling Intelligent Mode
■ Hot start
■ Jet Cool/Heat
This mode allows you to cool indoor air quickly in summer or warm it quickly
in winter.
- In jet cooling mode, strong air blows out at a temp. of 18°C for 30 minutes.
- In jet heating mode, strong air blows out at a temp. of 30°C for 30 minutes.
At the beginning of Fuzzy mode operation, the setting temperature is automatically selected
according to the intake air temp at that time.
When the Fuzzy key (Temperature Control key) is input, the initial setting temperature is selected,
the Fuzzy key value and the intake air temperature at that time are compared to select the setting
temperature automatically according to the Fuzzy rule.
While in Fuzzy operation, the airflow speed of the indoor fan is automatically selected according
to the temperature.
The indoor fan stops until the evaporator piping temp. reaches 29℃ (optional).
During heating operation, if piping temp. falls below 26℃(optional) the indoor fan will stop.
-57-

## Slide 6
Breakthrough Innovation
HVAC & Energy Solution
6.Trouble Shooting Guide
■ Auto Restart
ON/OFF
Button
-This function is useful in the situation of power failure.
When power regains after a failure this feature restore the previous
operating condition and the air conditioner will run in the same settings
This function is enabled by factory default setting. But you can disable
it by pressing the ON/OFF button for 6 seconds.
-The unit will beep twice and the lamp will blink 6 times. To enable it,
press the button again for 6 seconds. The unit will beep twice and
the blue lamp will blink 4 times.
- Comp and Outdoor fan stop when indoor evaporator pipe temperature is below 0℃ and restart
when the pipe temperature is above 7℃.
■ Eva Frosting Prevention
■ Compressor 2or 3 minutes Delay
- In the case when the compressor restarts after compressor off, there is time delay of 3-min. in order
to prevent damage to compressor due to frequent ON/OFF .
- Once OFF, the indoor unit fan will start with a delay of 5 seconds in order to prevent noise which
may be caused if the vane opening time and the fan start time are the same.
- Loads such as Fan speed control , Compressor, Timer etc are activated 2~ 3 seconds after
the corresponding key is pressed on the Remote controller .
■ Indoor Fan Start 5 seconds Delay
■ Function Activation Delay Time
-58-
Dehumidification
Heating
Cooling/Fan Mode
■ Different angle of vane for each operation mode
R.Control
Display
Mode
Sleep Mode/AutoClean
/

## Slide 7
Breakthrough Innovation
HVAC & Energy Solution
6.Trouble Shooting Guide
- With heat pump model, cooling and heating operation is changed automatically on the basis of the
room temp.
■ Auto Changeover
-59-
Initial Setting Temp: 22℃ (Memorize the final setting temp)
Control of setting temp.
- Wireless Remote Controller: 18-30 ℃.
- Reset Button in indoor unit: memorized final temp.
- Variation : -2 to + 2 ℃

## Slide 8
-60-
Check the difference in the intake and outlet air temperature
Check the gas side pressure
NORMAL
Inefficient compressor
Insufficient refrigerant
Clogged EEV or capillary tube
Low
Low
Low
Turn On the Unit
(by Remote Controller)
Open the front grille,try to turn on the unit by ON/OFF switch
Is there a large operating noise & vibration
YES
Check the output voltage of power transistor
Check installation condition
Make sure the required spaces
for installation[Refer page:25]
Check the power supply.Is there a power failure?
Has a breaker been turned off or a fuse blown?
Possibility of damaged Outdoor Unit PCB.
Make sure that the rated voltage
is supplied.[AC 208~230V, 60Hz ]
Check fuse condition & connection
wires.Make sure there is no electric short
[Refer page 34~36]
Less than 8℃ (cooling)
Or 14℃ (heating)
More than
8℃(cooling)
or 14 ℃(heating)
NO
NO
YES
NO
YES
Possibility of malfunction
Compressor/fan motor[Page 73,74]
Make sure that the installation
process is properly done
[Refer page: 43]
Make sure to check PCB condition &
refer to page 75 on how to measure
IPM circuit
EEV:Electronic Expansion Valve
Is there any Error
Code being displayed?
Check for the displayed error code.
Indoor Error: refer page 68
Outdoor Error: refer page 70
YES
NO
ON/OFF
Switch
6.Trouble Shooting Guide
6.1.3 Symptoms Overview
Is there any Error
Code being displayed?
NO
Check for the displayed error code.
Indoor Error: refer page 68
Outdoor Error: refer page 70
YES
Does Compressor/Outdoor Fan operate?
Refer <Trouble 3> page 64 for further instruction
NO
YES
Refer page 46 on how to read
a pressure manifold
Refer to <Trouble 2>
Unit doesn’t operate according to remote controller (page 63)
Refer to <Trouble 1> Unit doesn’t operate at all(Page 63)
Unit ON
Unit OFF
Unit OFF
Unit ON

## Slide 9
Breakthrough Innovation
HVAC & Energy Solution
6.Trouble Shooting Guide/6.1.3 Symptoms Measures & Diagnosis
Case | Explanation
Operation does not start immediately - When starting the unit just after it had been stopped. - When the mode(Cooling/Heating) was reselected. | This is to protect the air conditioner Wait for about 3 minutes
Hot air doesn’t come out at the start of heating operation | Air conditioner is warming up. Wait for 1 to 3 minutes (The system is designed to start discharging air only after it has reached a certain temperature)
Haze comes out of the indoor unit | Happens when the air in the room is cooled into mist by the cold airflow during cooling operation
Outdoor unit emits steam or water | Heating Mode -The frost at outdoor unit melts into water or steam when the air conditioner is in defrost operation Cooling Mode - Moisture in the air condenses into water on the cool surface of outdoor unit piping and drops
Case | Check
The unit doesn’t operate (Display LED is off) | Has a breaker been turned Off or a fuse blown? Is there a power failure? Are fresh batteries installed in the remote controller? Is the timer setting correct?
Poor Cooling/Heating effect | Are the filters clean?  See page 115 on how to clean the filters Is anything blocking the air inlet/outlet of the indoor&outdoor units? Is the temperature setting appropriately? Are the windows and doors closed? Are the airflow and its direction set properly?
Operation suddenly stops (Display LED is on) | Are the filters clean? See page 115 on how to clean the filters Is anything blocking the air inlet/outlet of the indoor&outdoor units? Turn the electric breaker off, clean the air filters or remove obstacles.Then turn the breaker on again & try operating the unit with the remote controller.If the lamp still blinks, check for error code in Trouble Shooting section.
Re-Check List
Symptoms which are not operational problems
-61-

## Slide 10
Breakthrough Innovation
HVAC & Energy Solution
6.Trouble Shooting Guide
Check the voltage of power (AC 208~230V, 60Hz)
The voltage of main power.
The voltage applied to the unit.
The connecting method of Indoor/Outdoor
connecting cable (each color)
Outdoor PCB Assembly
(Fuse, Noise Filter, Power Module (SMPS), IC01D, IC04D)
Primarily, the operating
condition of Micom is O.K
Check Indoor PCB CN-DISP1
The operation check of the PCB Assembly
Procedure
Remedy
Specification
1) The input voltage of Power
Module (SMPS)
2) The output voltage of Power
Module( SMPS)
3) IC01D(LD1085), IC04D(7805)
Replace the P.C.B
: DC 220V~390V
: 15V ±10%
: DC 5V
<Trouble 1>
Unit doesn't operate at all.
Turn off the main power and wait until LED on outdoor PCB is off.
Turn on main power again.
Does “Beeping” sound is made from the indoor unit?
Does “Lighting” LED is mounted on the outdoor PCB?
NO
YES
6.1.4 – Symptoms Measures & Diagnosis-Air Conditioner System (Electronic Parts)
-62-
P
W
V
U
Check for short
N
w
N
v
N
u
27
26
25
24
23
22
21
P
W
V
U
Nu
Nv
Nw
SPM3
[ IPM Pin Arrangement and
Pin Numbers]
2KW Controller

## Slide 11
Breakthrough Innovation
HVAC & Energy Solution
6.Trouble Shooting Guide
Turn on main power
While the compressor has been stopped, the compressor does not operate
owing to the delaying function for 3minutes after stopped.
When the compressor stopped Indoor fan is driven by a low speed.
At this point the fan speed is not controlled by the remote controller.
(When operated in the Sleeping Mode, the wind speed is set to the low speed as force)
Caused by the remote controller.
When the mark( ) is displayed in LCD
Screen, replace battery.
Caused by other parts
Check the contact of CN-DISP 1,2 connector
(Refer below PCB picture)
Check DISP PCB Assembly
- voltage between CN-DISP ③-⑧ : DC+5V
Check Point
Check the connecting circuit between
MICOM PIN 27 and CN-DISP1 PIN⑦
Check receiver Assembly
<Trouble 2>
Unit doesn't operate according to the remote controller
-63-
Main PCB
Disp PCB
CN-DISP 2

## Slide 12
Breakthrough Innovation
HVAC & Energy Solution
6.Trouble Shooting Guide
Turn on the Main Power
Operate "Cooling Mode( )" by setting the desired temperature of the remote controller at least 1.5℃ higher than the indoor side temperature
Compressor/Outdoor Fan is stopped during Air Circulation Mode
Check the sensor for indoor temp sensor whether it is attached as close as to be effected by the temperature of Heat Exchanger(HEX) or not
When Error Code is displayed, refer to the error code table in t/shooting guide section
Turn off Main Power
Check the electrical wiring diagram of outdoor side
Check the connection wires between indoor and outdoor
<Trouble 3>
Compressor/Outdoor Fan doesn't operate
Check the main power source. (AC 208V~230V)
Check the t/ shooting guide error code 21,26
Check that CN_FAN supplied voltage to outdoor PCB is about AC208V~230V
-64-

## Slide 13
Breakthrough Innovation
HVAC & Energy Solution
6.Trouble Shooting Guide
<Trouble 4>
Indoor Fan does not operate
Turn off the main power
Check the connection of CN-FAN
Check the Fan Motor
Check the Fuse(AC250V, T2A)
Check the circuit of indoor Fan Motor.
The pin NO. 38 of micron and the part for driving SSR(Solid State Relay). (Q01M)
Check the related pattern.
Check the SSR.
- SSR Open : Indoor Fan Motor will not operate.
- SSR short : Indoor Fan Motor operates in case of ON or OFF
Turn on the main power
Check the SSR high speed operation by remote
control (Indoor Fan Motor is connected).
The voltage of Pin No1(orange) and 3(balck)
of CN-FAN
Approximately 160V over
SSR is not damaged
Approximately 50V over
Check SSR
-65-

## Slide 14
Breakthrough Innovation
HVAC & Energy Solution
6.Trouble Shooting Guide
If there is no problems after above checks
• Check the assembly conditions and make sure that there are no interfering parts
in the rotation radial of the Vertical Louver
• Verify that the Vertical Louver is geared with the shaft of stepping motor.
• If the regular torque is detected when rotating the Vertical Louver with hands → Normal
• Check the connecting condition of CN-U/D Connector
• Check the soldering condition(on PWB) of CN-U/D Connector
Check the operating circuit of Vertical Louver at Indoor PCB
• Confirm that there is DC +12V between pin ① (RED) of CN-U/D and GND.
• Confirm that there is a soldering short at following terminals.
- Between 60,61,62 and 63 of MICOM
- Between 2,3,4 and 5 of IC01M
- Between 15,14,13 and 12of IC01M
<Trouble 5>
Vertical Louver does not operate
-66-

## Slide 15
Breakthrough Innovation
HVAC & Energy Solution
6.Trouble Shooting Guide
<Trouble 6> Heating Mode is not operating
In heating mode, the indoor fan will only operate when the pipe temperature is higher than 28°C.
Check the connector of intake and pipe sensor
• Check the related circuit of RY-4WAY
• Check the indoor room sensor whether it is disconnected or not.
• Check the indoor pipe sensor whether its disconnected or not.
Turn On the Main Power
Operate “Heating Mode ( )” by setting the desired temperature of the remote controller higher than one of the indoor temperature by 3°C at least.
About
DC 12V
Check the DC voltage on the PCB ASSEMBLY
• Comp Relay.
Check point
Between Micom
(NO.59) and GND
Between IC01M
(NO.11) and GND
Comp ON
DC 5V
Below
DC 1V
Comp OFF
DC 0V
About
DC 12V
Between Micom(NO.51) and GND
Check point
Between IC02M(NO.11) and GND
4 way ON
DC 5V
Below DC 1V
4 way OFF
DC 0V
About DC 12V
• 4 way Relay
• Outdoor fan Relay
Between Micom
(NO.53) and GND
Between IC02M
(NO.12) and GND
Fan ON
DC 5V
Below
DC 1V
Fan OFF
DC 0V
Check point
• Check the electrical wiring diagram of outdoor unit.
• Check if there is any abnormal condition concerning Compressor / Outdoor Fan Motor, 4 way.
• Check the connection wires between indoor and outdoor unit.
Turn Off the Main Power
-67-

## Slide 16
Breakthrough Innovation
HVAC & Energy Solution
6.Trouble Shooting Guide
• The function is to self-diagnosis air-conditioner and express the troubles identically if there is
any trouble.
• If more than two troubles occur simultaneously, primarily the highest trouble of error code is expressed.
• After error occurrence, if error is released, error LED is also released simultaneously.
• To operate again on the occurrence of error code, be sure to turn off the power and then turn on.
• Having or not of error code is different from Model.
■ Error Indicator
■ Indoor unit error – Descriptions
Error code | Description | Error indication | 
 |  | Indoor unit | 
 |  | LED1 | LED2
1 | Indoor Sensor (Air) open/short | 1 Time | -
2 | Indoor Sensor (Entry Pipe) open/short | 2 Times | -
5 | Communication Failure (Indoor Unit ↔ Outdoor Unit) | 5 Times | -
6 | Indoor Sensor (Exit Pipe) open/short | 6 Times | -
9 | EEPROM ERROR (Indoor Unit) | 9 Times | -
10 | Indoor Unit Fan Lock (Operation Failure) | - | 1 Time
12 | Indoor Sensor (Middle Pipe) open/short | 2 Times | 1 Time
6.1.5 Error Code & Descriptions
1) SB,SC chassis
2 )SH chassis
3) SE,S8,SD
-68-
SE
1 Digit
10 Digit

## Slide 17
Breakthrough Innovation
HVAC & Energy Solution
-69-
6.Trouble Shooting Guide
[Main PCB]
[Main PCB]
[Sub A PCB]
6.1.6 Indoor unit
[Sub A / Sub B PCB]
SB Chassis Indoor PCB(Printed Circuit Board)
-Picture: SB Libero R [Model Name:ASNH 09/12GB1U0]
SC Chassis Indoor PCB(Printed Circuit Board)
-Picture: SC Libero R [Model Name:ASNH 18/24 GC2U0]
※For more details, refer to each model’s wiring diagram in Service Manual

## Slide 18
Breakthrough Innovation
HVAC & Energy Solution
6.Trouble Shooting Guide
LED2
Red, 10 Digit
LED1
Green,1 Digit
1) 2 LED Type
2) 1 LED Type
■ Outdoor unit error – LED Location
Green
Red
■ Error Descriptions
4kw Controller(UE,UE1)
2kw Controller(UL,UL2)
1.5kw Controller(UA3)
2 LED Type
2 LED Type
1 LED Type
Ex) Error Code 21 (DC Peak)
1Sec
2Secs
2Secs
2Secs
2Secs
1Sec
1Sec
1Sec
-70-

## Slide 19
Breakthrough Innovation
HVAC & Energy Solution
6.Trouble Shooting Guide
Error Code CH01, CH02, CH06,CH12
Error code | Title | Cause of error | Check Point
01 | Indoor air sensor | Poor Connection Open / Short | Check sensor connection status Normal resistor : 10㏀ /at 25℃(77℉)
02 | Indoor inlet pipe sensor | Poor Connection Open / Short | Check sensor connection status Normal resistor : 5㏀ /at 25℃(77℉)
06 | Indoor outlet pipe sensor | Poor Connection Open / Short | Check sensor connection status Normal resistor : 5㏀ /at 25℃(77℉)
12 | Indoor middle pipe sensor | Poor Connection Open / Short | Check sensor connection status Normal resistor : 5㏀ /at 25℃(77℉)
1.Check if the temperature connection part is securely connected.
2.After disconnecting from temperature sensor PCB assembly, measure each sensor’s resistance
3.If the measurement indicates infinite or 0Ω please replace temperature sensor.
4.If the measurement is normal. then please check main indoor PCB and replace
Middle pipe sensor
Outlet pipe sensor
Inlet pipe sensor
Air sensor
6.1.6 Trouble Shooting / Error Code (Indoor Unit)
Error code | Title | Cause of error | Check Point
09 | Option PCB error | Poor connection of option PCB | Check the connection status of the option PCB
1. Check the option PCB is properly connected
Error Code CH09
-71-

## Slide 20
Breakthrough Innovation
HVAC & Energy Solution
6.Trouble Shooting Guide
Error Code CH05, CH53
Error code | Title | Cause of error | Check Point
05 / 53 | Communication (Indoor → Outdoor) | The communication between indoor<-> outdoor unit is stopped for more than 3 minutes | Power input AC 208~230V.(Outdoor, Indoor) The connector for transmission is disconnected The connecting wires are misconnected. The GND 1,2 is not connected at main GND. The communication line is shorted at GND. Transmission circuit of outdoor PCB is abnormal. Transmission circuit of indoor PCB is abnormal.
*CH05 is displayed at indoor unit, CH53 is displayed at outdoor unit
1. Check the input power AC 208~230V.(Outdoor, Indoor)
2. Check the communication wires are correctly connected.
→ Adjust the connection of wire
→ Confirm the wire of “Live”, “ Neutral”
3. Check the resistance between communication line and GND. (Normal : Over 2㏁)
4. Check the connector for communication is correctly connected.
5. Check the connection of GND, GND2, and main GND.
-72-