Blomberg washing machine.

01

Water inlet fault detected - washing machine will not fill

Check water supply to the washing machine is on

Check fill hose is not kinked

Check inlet valve filter

Check water inlet valve

02

Drain error detected - washing machine will not drain

Check drain pump filter

Check drain pump for blockage or restriction

Check outlet hose for blockage or obstruction

Check drain pump operation

Check drain pump wiring

03

Heating error detected - washing machine will not heat water

Check wiring to wash heater and thermostats

Check wash heater

Check thermostats

04

Motor triac shorted

Check motor connector block

Check wiring

Check electronic control

05

Temperature NTC error detected

Check temperature sensor wiring

Check temperature sensor

06

Motor tacho fault

Check motor connector block

Check wiring

Check motor carbon brushes

Check tacho connections

Check motor

07

Door latching or lock error

Door not detected closed

Check door is closed

Check door catch and latch

Check door lock wiring

Check door lock

09

Program selector fault

Check program selector connector

Check wiring

Check electronic control

10

Overfill detected - washing machine fills with too much water

Check level sensor connector block

Check wiring

Check electronic controller

11

Water heating fault detected - washing machine does not heat water

Check wiring to wash heater and thermostats

Check wash heater

Check thermostats

12

Door latch fault detected

Check door is closed

Check door lock connector block

Check wiring

13

Spin speed error detected

Check washing machine drive belt

Check motor connector block

Check wiring

Check motor carbon brushes

Check tacho connections

Check motor

18

Incorrect mains frequency or voltage

Check mains electricity supply

More Blomberg Washing Machine Help, Advice And Guidance